## Slide 1
01
COMP213 · Operating Systems
Computer
System
& OS Overview
Foundational Journey Through Hardware & OS
Principles
August , 2026
Xing Zheng / Dylan

## Slide 2
02
Chapter 1 · Computer System Overview
What is a Computer System?
A computer system has four core structural elements that work together
Processor
Controls operations and
processes data (your CPU)
Memory
Stores programs and data
temporarily while running
I/O Modules
Connects to external
devices: keyboards, disks,
networks
System Bus
The communication
highway linking all
components
4

## Slide 3
03
Chapter 1 · Computer System Overview
The Basic Instruction Cycle
Every program you run follows a simple but powerful loop
Fetch
Your CPU grabs the next instruction
from memory
Uses the Program Counter (PC)
Then
Execute
The CPU decodes and runs that
instruction
Move data • Calculate • Change flow
This cycle repeats billions of times per second — keeping your computer alive and responsive!

## Slide 4
04
Chapter 1 · Computer System Overview
Inside the CPU Registers
Let's look at three essential registers you'll work with
PC
Program Counter
Holds the address of the next
instruction to fetch from memory
IR
Instruction Register
Stores the current instruction being
executed by the CPU
AC
Accumulator
Temporary storage for arithmetic
operations and data
3

## Slide 5
05
Chapter 1 · Computer System Overview
A Program Execution Walkthrough
Tracing how the CPU adds two values from memory: a step-by-step demonstration
01
Fetch Stage
CPU retrieves instruction from
address stored in Program
Counter (PC)
02
Execute Stage
Performs operation (load, add,
store) using Accumulator (AC) as
working register
03
Store Result
Final sum written back:
memory[940] + memory[941] →
memory[941]
mem[940]
value A
+
mem[941]
value B
=
mem[941]
SUM

## Slide 6
04
Chapter 1 · Interrupts
Why Interrupts Matter
Problem
Without Interrupts
The CPU idles—wasting millions of cycles—while
waiting for slow devices like printers or disks to finish
Solution
With Interrupts
The CPU delegates I/O tasks and immediately resumes
useful work
When the device finishes, it interrupts the CPU to signal
completion
What would happen if your laptop froze every time you saved a file?

## Slide 7
07
Chapter 1 · Computer System Overview
The Interrupt-Driven I/O Flow
Let's compare how your CPU handles I/O in two different ways
Program-Controlled I/O
CPU waits idly during slow device operations
→ Wastes CPU cycles
VS
Interrupt-Driven I/O
CPU continues useful work while device operates
→ Resumes when device signals completion
Which approach keeps your system more efficient?

## Slide 8
08
Chapter 1 · Computer System Overview
The Enhanced Instruction Cycle
Now we add an interrupt stage to the basic fetch-execute cycle
Fetch
Decode
Execute
Interrupt
Loop
What's New
After each execute phase, the processor
checks for pending interrupts before fetching the
next instruction
Why It Matters
This simple addition lets your computer handle
urgent events (keyboard presses, disk
completion) without wasting cycles waiting
Think About It
Why do you think the interrupt check happens
after execute but before the next fetch?

## Slide 9
09
Chapter 1 · Computer System Overview
Types of Interrupts
Four fundamental interrupt types that CPU handles during execution
Program
Triggered by your code—like division by zero,
illegal instructions, or accessing memory you
shouldn't
Timer
Sent by the CPU's internal clock so the OS can
run tasks regularly (e.g., scheduling)
I/O
Raised by devices to say "I'm done!" or
"Something went wrong!" after reading/writing
data
Hardware Failure
Caused by serious issues like power loss or
memory errors—rare but critical
4

## Slide 10
10
Chapter 1 · Computer System Overview
Handling Multiple Interrupts
When multiple interrupts occur simultaneously, systems must decide how to manage
them
Disable Interrupts
Temporarily ignore new interrupts while handling the
current one
Simple implementation
May miss time-critical events
Interrupt Priority
Allow higher-priority interrupts to preempt lower-priority
handlers
More responsive to urgent events
Adds system complexity
Which approach would you choose for a medical monitoring system versus a basic calculator?
Computer System Overview
10 / 42

## Slide 11
11
Chapter 1 · Computer System Overview
Ch1 Summary: Hardware Basics
Three fundamental concepts you must understand about computer hardware
organization
01
Four Core Components
A computer has four core parts:
processor (executes instructions),
memory (stores data/programs), I/O
modules (connect to external
devices), and the system bus (links
everything)
02
Fetch-Execute Cycle
Instructions run in a fetch-execute
cycle: the CPU fetches an instruction
(using the Program Counter),
decodes it (Instruction Register),
then executes it—often updating data
in registers like the Accumulator
03
Interrupts
Interrupts let slow I/O devices signal
the CPU without wasting cycles; the
processor pauses, runs an interrupt
handler, then resumes—keeping the
system efficient and responsive

## Slide 12
12
Chapter 1 · Computer System Overview
Think About It: No Interrupts?
What would happen to system performance and
responsiveness without interrupts?
Your CPU would waste thousands of cycles waiting for slow devices like printers or
disks
The whole system would feel unresponsive—like your mouse or keyboard freezing
during file transfers
How would YOU design a better solution?

## Slide 13
03
Chapter 1 · Computer System Overview
The Memory Hierarchy Concept
Memory Pyramid Structure
Fastest, smallest, most expensive (registers,
cache) at the top → slowest, largest, cheapest
(disk, tape) at the bottom
The Trade-off
As speed ↑, size ↓ and cost per byte ↑. You must
balance these factors
Registers
Cache
Main Memory
Secondary Storage
Tape / Offline Storage
Speed ↓
Size ↑
Cost ↓
Why can't we just use the fastest memory everywhere?

## Slide 14
14
Chapter 1 · Computer System Overview
Why Caches Exist
Principle of Locality
Programs tend to access the same or nearby memory locations repeatedly
Temporal Locality
Accessing the same memory locations
repeatedly over time
Recent past → Near future
Spatial Locality
Accessing nearby memory locations in
close succession
Close addresses → Sequential access

## Slide 15
15
Cache Memory · Performance Optimization
How Cache Memory Works
Mapping
How main memory blocks are placed
in cache
Direct · Associative · Set-
associative
Replacement
Which block to evict when cache is full
LRU · FIFO · Random
Write Policy
How writes are handled to maintain
consistency
Write-through · Write-back
Which policy combination would work best for a mobile device with limited battery?
3

## Slide 16
16
Chapter 2 · Operating System Overview
Direct Memory Access (DMA)
CPU
DMA Controller
Memory
I/O Device
Data Transfer
Bypassing CPU
What it is
A dedicated DMA controller handles data transfers between I/O
devices and memory—bypassing the CPU entirely
Why it matters
Frees the CPU to do useful work instead of waiting during slow,
bulk transfers (e.g., disk reads)
Key benefit
Boosts system efficiency by reducing CPU overhead for large
data movements
Think About It
What would happen if the CPU had to copy every byte from
a hard drive?

## Slide 17
17
Chapter 1 · Computer System Overview
From Single Core to Multicore
This evolution enables true parallel processing capabilities
01
Single-Core
One processor handling all tasks
sequentially in early systems
02
SMP
Multiple processors sharing
memory, managed by one OS
03
Multicore
Multiple cores on a single chip,
each acting independently
Discussion Question
How might software need to change to take advantage of multiple cores?
3

## Slide 18
RECAP
Chapter 1 · Computer System Overview
Recap & Discussion Questions
01
Memory Hierarchy & Cache
Faster, smaller caches exploit locality to bridge the CPU-memory speed gap
Why can't we just use all cache instead of DRAM?
02
DMA & Multicore
DMA frees CPU from I/O data copying; Multicore chips enable parallel threads
How might DMA and multicore features interact in a real system?
?
?

## Slide 19
19
Chapter 2 · Operating System Overview
What is an Operating System?
Two fundamental roles that define every OS
Resource Manager
Allocates CPU time, memory, disk space, and I/O
devices fairly and efficiently among competing programs
Control Program
Supervises execution of user programs to prevent errors
and manage hardware access safely
Think About It
What would happen if
applications could directly control
hardware without an OS?
2

## Slide 20
20
Chapter 2 · Operating System Overview
Core OS Objectives
Every operating system aims to balance three key goals
01
Convenience
Making the computer easy to use through clean abstractions and intuitive
interfaces
02
Efficiency
Maximizing resource utilization (CPU, memory, I/O) without waste
03
Evolvability
Allowing the system to adapt and grow with new hardware and software
needs
Think About It
Which of these goals matters most for your smartphone's OS?

## Slide 21
03
Chapter 2 · Operating System Overview
Essential OS Functions
The OS handles six core jobs to keep everything running smoothly
Process Management
Creates, schedules, and terminates running
programs
Memory Management
Allocates RAM fairly and keeps processes
isolated
File Management
Organizes, stores, and retrieves your data
reliably
I/O Management
Controls communication with devices like
disks and keyboards
Protection
Enforces security rules so programs don't
interfere with each other
User Interface
Provides shells or GUIs so you can actually
use the system
6

## Slide 22
02
Chapter 2 · Operating System Overview
The OS as a Service Provider
Think of the operating system as your program's personal assistant — your code simply requests services
from the OS
Process Management
Creating and scheduling program
execution
Memory Allocation
Providing safe, isolated memory
space
File Operations
Reading/writing data without
knowing disk details
I/O Handling
Managing printers, keyboards, and
network devices
What would happen if every application had to manage hardware directly?
4

## Slide 23
23
Chapter 2 · Operating System Overview
Early OS: Serial Processing
01
No Operating System
Programmers worked directly with
bare metal hardware — no
software layer in between
02
Sequential Execution
Each program ran one after
another: load → execute → unload
before the next job
03
Manual Operation
You had to manually set switches
or punch cards for every single
instruction
What challenges would you face if you had to operate a computer this way today?
23

## Slide 24
02
Chapter 2 · Operating System Overview
Simple Batch Systems
01
Batch Processing
Groups similar jobs together to reduce setup time between tasks
02
The Monitor
Early OS automatically loads and runs the next job in sequence
03
Improved Efficiency
Eliminates manual intervention between jobs, improving CPU
utilization
Think About It
How would you design a system to
handle different types of jobs fairly?
?
\"
24 / 42

## Slide 25
25
Chapter 2 · Operating System Overview
Multiprogramming Revolution
Multiprogramming keeps several jobs in memory at
once, so when one job waits for I/O, the CPU can
immediately switch to another ready job
Dramatically boosts CPU utilization
CPU Utilization Comparison
Single Job
CPU
I/O Wait
CPU
I/O Wait
Multi-Job
Job 1
Job 2
Job 3
Job 1
← CPU stays busy! No more idle time →
Think About It
What happens if we only run one job at a time? How much CPU time goes to waste?

## Slide 26
26
Chapter 2 · Operating System Overview
Time-Sharing & Multitasking
Core Concept
Time-sharing lets multiple users interact with a
computer simultaneously by rapidly switching
the CPU between their jobs
1
Each user gets the illusion of having exclusive machine access
2
Switching happens so fast (milliseconds!) that you won't notice
delays
3
This evolved from batch processing to enable interactive
computing
Think About It
What would happen if the OS didn't
switch tasks quickly enough?
How slow is "too slow" for you to
feel it's unresponsive?
26 / 42

## Slide 27
27
Chapter 2 · Operating System Overview
Modern OS Milestones
01
Microkernels
Move core services out of kernel space —
improves modularity and security
02
Multithreading
Let a single process run multiple threads —
boosts responsiveness & CPU utilization
03
SMP Support
Manage Symmetric Multiprocessors —
multiple CPUs sharing memory for scalability
04
Object-Oriented Design
Structure OS components as reusable objects
— eases maintenance & extension
Think About It
How might these ideas shape the OS you'll build?
?

## Slide 28
28
Chapter 2 · Operating System Overview
Summary: OS Evolution
01
Serial Processing
No OS: Programmers ran one job at a time directly on hardware
02
Multiprogramming & Time-sharing
OS emerged to manage resources, enable concurrency, and
support interactive use
Modern OS Foundation
Critical Thinking
Each step solved real
limitations. What if we
skipped
multiprogramming—could
modern apps even exist?

## Slide 29
29
Chapter 2 · Operating System Overview
Imagine This:
No
OS?
What if you had to manually:
Load programs into memory
Switch between applications
Manage CPU time fairly
Handle I/O operations directly
How would you keep everything running smoothly—without crashing?
29 / 42

## Slide 30
30
Chapter 2 · Operating System Overview
Major OS Achievements
Modern operating systems solve three fundamental challenges that define computing
01
Process Management
Creating, scheduling, and
coordinating multiple programs so
they run smoothly together
02
Memory Management
Giving each program its own
"private" memory space while
efficiently sharing physical RAM
03
Information
Protection
Controlling who can access what
resources to keep the system secure
and stable
3

## Slide 31
31
Chapter 2 · Operating System Overview
Process Management Basics
The operating system treats each program as a process—a unit of work that it manages
from start to finish
Creates
Starts a new process when you launch
a program
Schedules
Decides which process runs on the
CPU and when
Terminates
Ends the process cleanly when it's
done or crashes
Think About It
What might happen if the OS couldn't terminate a stuck process?
3

## Slide 32
32
Chapter 2 · Operating System Overview
Memory Management Goals
Your OS needs to balance three key goals when managing memory
Isolation
Keep each process's memory separate so bugs or attacks in one
program can't affect others
Sharing
Allow processes to safely share memory when needed (like
shared libraries)
Efficient Usage
Make the most of limited RAM by using techniques like virtual
memory
Discussion Question
How would you design a system that
achieves all three goals at once?
3

## Slide 33
03
Chapter 2 · Operating System Overview
Virtual Memory Concept
What Process Sees
Virtual Address Space
Each process believes it has its own huge, private memory
OS Maps Behind the Scenes
Physical Reality
Physical Memory (RAM)
Limited hardware memory shared by all processes
Address Space Illusion
Each process gets its own huge, private address space
—even when physical RAM is limited
Address Translation
OS maps virtual addresses (used by programs) to
physical addresses (in real memory)
Process Isolation
Every process gains isolation and the feeling of
abundant memory
How would programs behave if they shared one global address space?
33 / 42

## Slide 34
34
Chapter 2 · Operating System Overview
Information Protection & Security
Access Control
Mechanisms decide who can use what
resources
Protected Space
Each process runs in isolation – you
can't mess with others' data
Permissions
The OS enforces read, write, execute
– like digital locks on files
How would your phone feel if any app could read your messages or delete photos?
3

## Slide 35
35
Chapter 2 · Operating System Overview
Scheduling Fundamentals
The OS uses a scheduler to decide which ready process gets the CPU next — like a traffic cop
managing flow through an intersection
1
The Scheduler
A critical OS component that selects which process in the ready queue gets CPU time next
2
Ready Queue
Maintains all processes waiting for CPU — without scheduling, only one program runs at a
time
3
Scheduling Algorithms
Apply fair and efficient decision-making rules to allocate processor time among competing
processes
Scheduling Flow
Ready Queue
P1
P2
P3
P4
Scheduler
CPU
Critical Thinking
How would you design a fair system if you had to choose between urgent tasks and long-running computations?
35

## Slide 36
36
Chapter 2 · Operating System Overview
System Generation (SYSGEN)
What is SYSGEN?
System Generation is the process of
customizing and configuring an operating system
for a specific computer's hardware setup
When does SYSGEN happen?
01
Installing an OS on new hardware
02
The OS needs to recognize your exact CPU, memory, and
devices
03
Drivers and kernel modules are selected based on your system
Think About It
What might go wrong if an OS skips proper SYSGEN for your laptop?

## Slide 37
03
Chapter 2 · Operating System Overview
Key Concepts
Four pillars that define modern operating systems
Processes
The OS manages programs as processes—isolated units of
execution with their own state and resources
Memory
Virtual memory gives each process the illusion of a large,
private address space, even on limited physical RAM
Protection
Hardware and OS mechanisms enforce access control,
ensuring processes can't interfere with each other or the kernel
Scheduling
The scheduler decides which ready process runs next,
balancing fairness, responsiveness, and throughput
How do these four pillars work together to make multitasking feel seamless?
4

## Slide 38
02
Chapter 2 · Operating System Overview
Puzzle This: Resource Sharing
How can the OS safely allow multiple processes to share the same printer?
01
Should processes send print jobs directly to the printer?
02
What could go wrong if two processes print simultaneously?
03
Could we use a queue to manage print requests?
04
What role does the OS play as a resource manager here?
38 / 42

## Slide 39
39
Chapter 2 · Operating System Overview
OS for Multiprocessor Systems
In SMP (Symmetric Multiprocessor) and multicore systems, the OS faces three key
challenges
Scheduling
The OS must distribute processes
across multiple CPUs fairly and
efficiently
Synchronization
Shared resources need careful
coordination to avoid race conditions
Memory Management
Ensures cache coherency and efficient
memory access across cores
How would you design a scheduler that balances load while minimizing inter-core communication
overhead?
3

## Slide 40
40
Chapter 2 · Operating System Overview
Modern OS Characteristics
Three key architectural innovations that define modern operating systems
Microkernel
Architecture
Keeps the kernel minimal—only
essential services (like IPC) run in
kernel mode. Everything else (drivers,
file systems) runs as user-space
processes for better stability and
security
Multithreading
Lets a single process have multiple
threads of execution, improving
responsiveness and enabling efficient
use of multicore CPUs
Object-Oriented Design
Treats system resources (files,
devices, processes) as objects with
defined interfaces—making the OS
more modular, reusable, and easier to
extend
3

## Slide 41
41
Chapter 1 & 2 · Summary
Final Recap: From Hardware to OS
The operating system transforms raw hardware complexity into usable abstractions
01
Raw Hardware
Your computer's hardware (CPU,
memory, I/O) is raw and complex—but
the OS hides this complexity through
abstraction
02
OS as Bridge
Think of the OS as a bridge: it turns
physical resources into easy-to-use
services like processes, virtual
memory, and files
03
Why It Matters
Without these abstractions, you'd
manage every register, interrupt, and
memory address yourself—imagine
coding that!
OS

## Slide 42
42
Chapter 2 · Operating System Overview
Let's Discuss & Explore!
Open questions for further exploration and critical thinking
Question 01
What if we redesigned
interrupts for today's multicore
systems—how would you
approach it?
Question 02
Where do you think operating systems
will evolve next as hardware keeps
changing?
Question 03
If you were building an OS from
scratch today, what would be
your top priority?
?
千问AI生成